## Slide 1
Security Level:
Introduction to eSight 21.0 Network Resource Management

## Slide 2
This course describes how to use eSight to perform routine management, monitoring, and maintenance for network devices.

## Slide 3
Upon completion of this course, you will be able to:
  Have a good command of the management of network monitoring devices.
  Have a good command of routine network management, monitoring, and maintenance methods.

## Slide 4
Overview
1
Site Deployment
2
3
Routine O&M

## Slide 5: Typical Networking of Network Services
Campus network
Basic management
OSS
Third parties
NBI
SFTP
Telnet/STelnet
SNMP
Topology
management
Alarm
management
Performance
management
Resource
management
Configuration file management
eSight
Router, switch, WLAN, and firewall
Network O&M personnel
Browser (Firefox, and Chrome)
Central equipment room
Personal devices
R&D network
Administrative region
Access layer
Convergence layer
eSight

## Slide 6: eSight 20.1 Network Resource Management O&M Feature Overview
Basic monitoring
Resource management
Terminal management
Command configuration
Configuration file
Network O&M
Performance, alarm, and report
Device, subrack, and board
Backup and restoration
Discovering suspicious and unauthorized terminals
Batch delivery

## Slide 7
Overview
1
Site Deployment
2
3
Routine O&M

## Slide 8: Deployment Overview
Subnet planning
Device addition
Monitoring configuration
Categorize network devices by subnet to facilitate hierarchical monitoring.
Add the networks to be managed to eSight based on the SNMP and adjust their positions in the topology as required.
Subnet planning
Device addition
Monitoring configuration
(Optional) You can customize the configurations based on network conditions.
By default, performance collection tasks, large screens, and report data are preset and usable-upon-unpacking. You can adjust them as required.

## Slide 9: Subnet Planning
A large network is divided into several subnets based on a specific rule (by region or device type), which facilitates network management.
Generally, subnets are planned by region.
A device can belong to only one subnet.
The current subnet management is performed based on topology.
You can create, delete, or move a subnet only by right-clicking the blank area in the topology view.

## Slide 10: Device Addition
If SNMP parameters are correctly set for devices, you can add devices one by one, in batches, or by automatic discovery to the NMS for management.
Automatic discovery is applicable to batch addition of devices with consecutive IP addresses and the same SNMP parameter settings.
Adding devices one by one is applicable when the number of devices is small and SNMP parameters are different for the devices.
Batch import is applicable to various scenarios.

## Slide 11: Monitoring Configuration - Topology
1. In addition to manual dragging, default common layouts of topology icons are provided for flexible configuration.
2. Figures can be expanded for improved clarity.

## Slide 12: Monitoring Configuration - Performance
Preset performance monitoring policy
Creating a performance monitoring policy
Monitoring object group
1
1.1 Create a monitoring object group based on certain rules.
Performance monitoring service
2
Monitoring policy
2.1 Select monitoring indicators.
2.2 Select monitoring object groups or monitoring objects.
5
An alarm is generated when the threshold is exceeded.
Alarm management
portal
6
View top N collected data in the homepage portal.
2.3 Select a collection period.
3
Scheduled collection on the background
3.1 Automatic information collection
4
Performance data
4.1 View latest data.
4. 2. View historical data.
4.3 View real-time performance.
Various performance indicators are available. Performance monitoring policies can be extended as required.
Presets common KPI policies are usable upon unpacking. Automatic monitoring is started after devices go online.

## Slide 13: Monitoring Configuration - Polling Tasks
eSight provides customized configuration parameters to improve network management efficiency and quality.
Category | Scenario | Function | Default Value | Setting Notes
Between the NMS and devices | Device status polling | Check the connectivity between the NMS and devices. | The interval is 30s. | You cannot change the parameter value.
 | Polling device inventory data | Periodically synchronize all device information. | Start time: 2:20; duration: 4 hours | Full synchronization consumes system resources. Therefore, you are advised to perform full synchronization during off-peak hours, for example, in the early morning.
 | Interface status polling | Periodically check the status of link interfaces or network-wide interfaces. | No polling | It is recommended that this function be used when the alarm channel is abnormal or the alarm synchronization function is invalid. Set this parameter based on the number of devices. The larger the number of devices, the longer the polling interval.
 | Terminal data polling | Periodically obtain wired terminals and their statuses. | Every 1 hour | You cannot change the parameter value.
 | Backing up configuration files | Periodically obtain configuration files from devices. | Unstarted | You are advised to back up key devices once a day.
Operations on this page are professional. You are advised to perform these operations under the guidance of professional personnel.
Polling/Reconciliation

## Slide 14
Overview
1
Site Deployment
2
3
Routine O&M

## Slide 15: Routine O&M of Network Devices - Resource Overview
Device status statistics. You can click the rose chart to quickly filter devices.
Go to the details page of a single device and view the detailed information about the device, including alarms, KPIs, and interfaces.
Column customization. Many columns are available, including maintenance information.

## Slide 16: Routine O&M of Network Devices - Key Device Monitoring
Basic device information
Device KPIs, which are marked in red if they exceed the thresholds
Connections between a single device and peripheral devices
Alarm statistics of a single device
Key resources: interface, power supply, and fan status statistics.

## Slide 17: Routine O&M of Network Devices - Device Panel
The high-fidelity Huawei device panel displays devices at a ratio of 1:1. You can right-click the panel to quickly perform operations.
The low-fidelity third-party device panel displays the interface statuses.

## Slide 18: Routine O&M of Network Devices - Interface
Interface information is displayed based on matrices.
Logical sub-interfaces are not displayed.
Interface names and details are displayed.
Interface resource information is displayed, including IP addresses, Ethernet-trunk relationships, and link relationships.

## Slide 19: Routine O&M of Network Devices - VLAN
View, add, and delete interfaces that can connect to the VLAN.
View and remove VLAN member devices.

## Slide 20: Routine O&M of Network Devices - Configuration File Management
O&M principle: To ensure network stability, minimize device configuration changes. When device configurations on a network change, O&M engineers must be aware of the change, check whether the change is valid, and take measures in a timely manner to prevent the network from being attacked or modified illegally.
O&M engineers
Deployment of periodic tasks
Periodic backup
Alarm
Configuration file restoration
Baselined files
Is the change valid?
Is the configuration changed?
Yes
No
Valid
Invalid
Alarm notifications can be sent to customers via SMS messages or emails.

## Slide 21: Routine O&M of Network Devices - Configuration File Management
Users can quickly view the latest configuration files and download them to the local computer for archiving.
The differences in the configuration file are marked in red. You can quickly check whether the changed content is valid.
Traverse the differences one by one to avoid repetition or omission.
Check the detailed backup file list on the device.

## Slide 22: Routine O&M of Network Devices - Terminal Monitoring
Terminal discovery principles
View the recovery suggestions.
Associate with the NE manager and device panel to quickly view the running status, performance indicators, and alarms of devices and ports and rectify terminal network faults.
1
2
Create a terminal access whitelist and bind terminal access rules
to generate alarms for unauthorized terminals.
Router-ARP table |  | 
port1 | ip1 | mac1
port2 | ip2 | mac2
port3 | ip3 | mac3
SW1-MAC forwarding table | 
mac1 | port1
mac2 | port2
Terminal A (mac1, ip1)
Terminal B (mac2, ip2)
Terminal C (mac3, ip3)
SW2-MAC forwarding table | 
mac3 | port3
Collects device MAC forwarding table and ARP table data

## Slide 23: Routine O&M of Network Devices - Command Configuration Tool
23Page
O&M method: Configuration operations on a large number of NEs are mandatory during network construction or reconstruction. Manually making scripts according to the network plan is time-consuming and error-prone. The command configuration tool of eSight allows users to use a configuration template and a plan sheet to deliver parameters in a batch to NEs by one click, improving NE configuration efficiency.
Create a template.
Select devices.
Configure an execution policy
View the task execution result